Task Scheduling in an Arduino Environment

Once you get to complex real time Arduino software, you may wish you had the task scheduling capabilities of a modern operating system. You can actually do that, by using a Real Time Operating system, such as FreeRTOS:
       ( https://create.arduino.cc/projecthub/feilipu/using-freertos-multi-tasking-in-arduino-ebc3cc )

Another approach is to implement a simple task scheduling system within the Arduino environment. What follows is a description of one approach to do that.

Some of the capabilities are:

- handles tasks that occur at a fixed frequency
- handles tasks that just need to be executed once (Like the forking concept in Linux)
- executes higher priority tasks first (without pre-empting)
- gives tasks initiated by interrupts top priority when multiple tasks can be executed
- allows tasks initiated by interrupts to be executed in the background before the next clock tick
- minimizes interrupt task latency due to waiting for other tasks to complete

Things this scheme can not do:
- pre-empt a running task to run a higher priority one. All tasks run to completion, once started, with interrupts occurring as required
- run a background handler triggered by an interrupt before the currently executing task has completed.

Design overview:

For discussion purposes, we’ll make the following assumptions:
- timers are based on an interrupt occurring every 20 microseconds, or a frequency of 50 KHz
- we have tasks T1_Task through T4_Task that each run at their own frequency, (T1_Freq...) , in Hz
- we have a task U1_Task that is executed on demand, perhaps after a delay, initiated by another task

Each task has a counter (T1_Cnt, T2_Cnt...) associated with it that tracks the number of timer interrupts remaining before the timer expires and the task is executed. This counter can have these values:

    -1 means the task is suspended and no timer is running

     0 means that the task is ready to execute.
        Task U1 would be requested by writing 0 to its counter

    +n means “n” more timer interrupts are needed before the timer expires and the task is run
        To execute a task 1 at T1_Freq, the counter is initialized to (1,000,000 / T1_Freq) / 20, or
        more simply, 50000 / T1_Freq

The timers are initialized to their interrupt count, and count downwards towards 0. This allows the time interval to be variable (when the timer is reset) and supports having a zero value for a task that another task wants to initiate.

NOTE: It is the responsibility of the task to reset the timer by putting a new value into it. This would typically be the timer length expressed in timer interrupts, but could be -1 to disable the task until further notice. Leaving the value at 0 will cause the task to be executed once per timer interrupt.

The Arduino loop() routine consists of code that checks for tasks to execute, and nothing else. It spends most of it’s time in a spin lock, wait for the timer interrupt to set a flag indicating that the next interrupt has occurred. When this happens, it scans down the list of tasks, decrementing the timer counter where appropriate, and executing tasks when appropriate.

This scan is done from top priority task to lowest priority, and the scan restarts at the top priority task every time a task is completed. This ensures that tasks initiated by interrupts or the previously running task itself get executed in priority order.

When no more tasks remain to be executed, the loop() routine returns to the spin lock, awaiting the next timer interrupt. The resulting code would look something like this:

long T1_cnt, T2_Cnt, T3_Cnt, T4_Cnt, U1_Cnt

volatile boolean saw_20usec_int, ran_a_task

long T1_Freq = 500; // long size allows task frequencies slower than once per hour
long T2_Freq = 250;
long T3_Freq = 200;
long T4_Freq = 100;

void setup() {
    T1_Cnt = 50000 / T1_Freq; // number of timer interrupts to achieve this frequency
    T2_Cnt = 50000 / T2_Freq;
    T3_Cnt = 50000 / T3_Freq;
    T4_Cnt = 50000 / T4_Freq;
    U1_Cnt = -1 // On demand task is suspended until needed
}

void IRAM_ATTR onTimer() {
    saw_20usec_int = TRUE; // let scheduler in loop() know we had an interrupt
// maybe do some stepper / wheel manipulations here as well
}

void T1_Task() {
    // ...processing associated with the task...
    // T1 decides we need to run task U1 after a delay of half a second
    U1_Cnt = 50000 / 2 ; // running every half second is same as 2 Hz
    // end of T1 task processing
    T1_Cnt = 50000 / T1_Freq ; // reset task timer
}

void U1_Task() {
     // ...processing associated with the task...
     U1_Cnt = -1 ; // suspend this task until it’s requested again
}

void loop() {

if(saw_20usec_tick == TRUE)
{ saw_20usec_tick = FALSE ; // prepare for interrupt to signal next tick
    ran_a_task = TRUE ; // set up for first scan through tasks

    while (ran_a_task == TRUE) // keep going until no tasks left to run
    { while ( 1 == 1 ) // dummy container loop so break gets back to top priority
        { ran_a_task = FALSE ; // initialize flag: so far, no task was executed

// adjust timer counter for T1 task, and see if it should run
        if (T1_cnt > 0 ) // if there's a counter running for the top priority task
        { T1_Cnt --= ; // decrement it
        }
        if ( T1_Cnt == 0) // if it got to 0, or already was 0, execute task
        { T1_Task ; //call the task, which would also set new value into T1_Cnt
        ran_a_task = TRUE ; // flag that we did run a task
        break ; // exit from inner while, which restarts the outer while
        }

// ... and so on, for all tasks, including the U1 task ...

        if (T4_cnt > 0 ) // if there's a counter running for priority 4 task
        { T4_Cnt --= ; // decrement it
        }
        if ( T4_Cnt == 0) // if it got to 0, or already was 0, execute task
        { T4_Task ; //call the task, which would also set new value into T4_Cnt
        ran_a_task = TRUE ; // flag that we did run a task
        break ; // exit from inner while, which restarts the outer while
        }

        if (U1_cnt > 0) // if there's a counter running for on-demand task
        { U1_Cnt --= ; // decrement it
        }
        if ( U1_Cnt == 0) // if it got to 0, or already was 0, execute task
        { U1_Task ; //call the task, which would also set new value into U1_Cnt
        ran_a_task = TRUE ; // flag that we did run a task
        break ; // exit from inner while, which restarts the outer while
        }
        break ; // no tasks were runnable, exit inner while with ran_a_task = FALSE

        } // while ( 1 == 1)

    } // while (ran_a_task == TRUE)

} if(saw_20usec_tick == TRUE)

} // void loop()