SB7 Circuit Board Checkout Steps

Goals:

- detect problems with
- circuit board manufacture
- component placement
- power cable connections
- verify that correct voltages appear in correct places on board
- verify DRV825 motor controller calibration
- confirm console cable connections are working properly

Setup:

- gather needed materials:
- chassis with
- battery connection soldered to cable with large black connector
- charged battery
- SB7D main circuit board
- fully populated
- with power cables on screw down terminals per git diagram SB7D-power-wiring.odg
- voltage regulator board with power cables on screw down terminals per same diagram

Steps:

- ensure all 6 power connectors are disconnected
- remove ESP32, DRV825 motor controllers and IMU from main board
- to make the left/right and top/bottom references that follow correct, orient the main board with ESP32 in top left corner
- check that all logic grounds on main board are connected:
- test point near IMU
- CPU pin 4 (bottom right of ESP32 board)
- LCD header ground pin (bottom right pin)
- left contact on 3 position regulator screw down terminal
- bottom left pin on each DRV825 motor controller
- second pin from the right on IMU socket
- check that battery grounds are connected:
- right contact on screw down terminal at bottom right for regulator input power
- left contact (away from corner) on screw down battery power connector at top right of board
- check that all 12V locations are connected:
- middle contact on 3 position regulator screw down terminal near bottom right corner
- bottom right pin on each DRV825 motor controller
- check that 20V locations are connected when white push button pushed in:
- left contact on 2 position screw down terminal in bottom right corner of board
- right contact on 2 position screw down terminal in TOP right corner of board
- verify that above 2 locations are disconnected if white switch is in the out position
- check for connectivity for these 5 V locations:
- right contact on 3 position regulator screw down terminal near bottom right of board
- 5V test point on push button switch contacts, as shown in power cable diagram
- check that there are no shorts between any of the 5 contacts on the 2 screw down terminals at the bottom right

- verify that the pullup for MOSFET is removed per lesson from previous board
- connect cable directly to ESP32 console and run a blinkly test program

TO BE CONTINUED - WORK IN PROGRESS